## Slide 1: The Experiment of kHz laser Ranging with Nanosecond Pulses at Shanghai
Shanghai Observatory, Chinese Academy of Sciences
Shanghai, China
Zhang Zhongping, Yang Fumin, Chen Juping,
Zhang Haifeng, Wu Zhibo, Qin Si, Li Pu

## Slide 2
The aim of the experiment is to test our design of kHz control system:
  Range Gate Generator board
  Event Timer
  Control software and data acquisition
  Data processing capability
2. We are pleased to get the support from national natural science foundation in China to research on kHz SLR.
3. We borrowed a kHz laser with long pulse width from North China Research Institute of Electro-Optics.
4. On Apr.26 2008, we successfully got returns from Ajisai satellite first time with kHz system. So far, the experiment has been done at ERS-2, Lageos etc. with 2mJ energy, 50ns pulse width laser.
Introduction

## Slide 3
Repetition: 1KHz (1-10kHz)
Pulse width:50ns
Energy per pulse: 2mJ
Divergence: 6mrad
Diode pumped oscillator
Size: 52*17*12cm**3
Made by North China Research
Institute of Electro-Optics
The kHz Laser: Main Specs
Laser
Control/driver
Beam Expander

## Slide 4
1、7 HR concave mirror; 2 acousto-optic device; 3 Nd:YAG rod;
4 focus lamp cavity; 5 output coupling mirror; 6 SHG; 8 polarimeter;
9 diode array
The sketch map of laser inner optical structure

## Slide 5
Single shot RMS: 10ps
FIFO: 12000 time-tags
A032-Event Timer
Made by Riga, Latvia
Measurement rate: up to 10KHz
Communication port: EPP mode

## Slide 6
We exploit the Event Timer functions to adapt for KHz ranging and develop our own data acquisition software with Visual C++, according to the sample program which defines device-specific software.
The schematic control diagram for A032-Event Timer

## Slide 7
We use two RGGs: one from Graz, another made by our group.
Graz RGG board: 0.5ns resolution, 1ns accuracy,
512 buffer, ISA mode
Shanghai RGG board: 5ns resolution. 1024 buffer,
EPP mode
At the begin of the experiment, Graz board is used.
After that, we use our board to measure satellites.
The kHz Range Gate Generators

## Slide 8
Layout of Shanghai Range Gate Generator
receive/transmit overlap occurring time
Range Gate
Laser Fire
200MHz
10MHz
Serial Port
EPP port
FIFO
Comparator
1pps
Serial module
EPP
module
FPGA (Xilinx,Spartan3,XC3S200)
RT clock
module
1pps Epoch Time
Expected Event Time of Return
DCM
Laser Firing module
Backscatter Avoiding

## Slide 9
Real Time clock module sync to UTC with 5ns resolution.
If Expected Event Time of Return equals to Real Time, then range gate is generated
If receive/transmit overlap occurring time equals to Real Time, then backscatter avoiding function of laser firing module is start.

## Slide 10: Method of backscatter avoiding
If < 100 us between Receive/ Transmit, Laser Firing will
be shifted by (120 us).
100us
Backscatter avoiding
Laser Firing
Prediction return pulse
receive/transmit overlap occurring time
Expected Epoch Time of Return
(120us)

## Slide 11
The kHz Control Software is designed and built by Shanghai Station. There are two computers used in the experiment in Windows OS:
One computer is used for communication with ET,
recording start and stop events, and matching them,
identifying, displaying residual (O-C), storing data, etc.
Another computer is used for tracking and controlling,
including laser firing, 1kHz range gating, receive and
transmit overlap avoiding, etc.
During the experiment, two computers communicate
with each other via RS232.
kHz Control Software System

## Slide 12: Block diagram of one kHz system
ILRS
P4
3.0G
512M
Windows
Serial #1
GPS
Serial #2
EPP
RGG
Laser
C-SPAD
I/O card
Timing/Tracking
Serial #3
Meteo para
Serial #4
P4 3.0G 512M Windows
Event Timer
Start
Stop
Fire
RG
EPP

## Slide 13: Time sequencing diagram of writing FIFO
∫
start1
start2
stop1
stop2
∫
stop1
stop2
∫
stop100
∫
Put 100 expected epoch time of return into FIFO once a 100ms in advance to satisfy real-time control software
∫

## Slide 14
Real-time tracking interface for tracking, firing…

## Slide 15
Return ID
Firing,return match,etc.
Residual
(O-C)
Return distribution statistics
Another computer’s real-time interface for recording start and stop events, displaying (O-C), etc.

## Slide 16: Data Pre-Processing
Selected obs. data screen
Full obs. data screen
Displaying selected obs. data on screen
Processing all data
Advantage: fast, not influence result.
Satellite: Stella
on May 1
153k recorded
24k returns

## Slide 17
Satellite: Ajisai
on May 1
618k recorded
190k returns
Pre-Processing screen

## Slide 18
Real-time interface for Lageos ranging
Satellite:
Lageos-1
on Sep. 9
900k recorded
60k returns
Valid data

## Slide 19
Satellite | KHz SLR |  | Routine SLR
 | Recorded | Returns | Returns
Ajisai | 618k | 190k | 1500
Stella | 153k | 24k | 500
BeaconC | 81k | 42k | 800
Lageos1 | 900k | 60k | 1000
  KHz SLR returns vs. Routine SLR
  at Shanghai station

## Slide 20: 1 kHz SLR experiment’s video (Ajisai, on May 1)

## Slide 21
Summary
We have successfully obtained returns from satellites (ajisai,stella,beaconC,ERS-2, Envisat, Lageos,etc.) by using a kHz laser with long pulse width. The experiment shows that 1 kHz control system works fine and promisefully.
Plan to purchase a kHz laser with short pulse width next year, and to start routine kHz ranging with high precision.

## Slide 22
Thank You !