## Slide 1
High speed Pockels Cell
shutter and the Herstmonceux MCP-PMT detector
Matthew Wilkinson
and the NERC Space Geodesy Facility team
Wednesday, October 15
Session 7 - High repetition-rate systems

## Slide 2
Introduction
The NSGF SLR system uses a C-SPAD detector and consequently makes only one detection per laser fire. Also the C-SPAD must be armed 50-100ns before an observation to avoid any bias.

## Slide 3
Introduction
If the C-SPAD detects a noise point before the arrival of the satellite return signal then the opportunity to observed the satellite for that shot is lost.
In comparison to the Nd:YAG laser, the new kHz laser system has a greatly reduced signal to noise ratio with much more sampling.
Therefore, daylight noise is much more apparent in the range gate window and has a more significant impact on observing.

## Slide 7
Daylight noise in the range gate
The C-SPAD will make a detection within a few hundreds of nanoseconds during normal daylight operations.
To reduce daytime noise the return path includes an oven controlled daylight filter that allows a narrow spectrum of 0.14nm FWHM centred at 532.1nm. Peak Transmission is 68.04%.
The following plot shows the daylight detections for the Champ pass as a proportion of laser fires.

## Slide 9
Very Fast Shutter
Introducing a shutter before the C-SPAD will allow it to fully arm in darkness. The shutter can then be opened much closer to the satellite track (~10ns).
This could turn a 50% loss to a 10% loss.

## Slide 10
Suitably Fast Shutters
Physical - Spinning disc or resonant forks opening and closing a physical barrier matched in phase.
Liquid Crystal Display - Cell containing long molecules aligned at each surface and 90 degrees apart. Polarised light is rotated through the cell with no applied voltage. Cell becomes opaque when a voltage is applied as the molecules align to the electric field.

## Slide 11
Suitably Fast Shutters
Physical - Spinning disc or resonant forks opening and closing a physical barrier matched in phase. However, it is demanding to match the kHz frequency and phase of the returning signal.
Liquid Crystal Display - Cell containing long molecules aligned at each surface and 90 degrees apart. Polarised light is rotated through the cell with no applied voltage. Cell becomes opaque when a voltage is applied as the molecules align to the electric field.

## Slide 12
Suitably Fast Shutters
Physical - Spinning disc or resonant forks opening and closing a physical barrier matched in phase. However, it is demanding to match the kHz frequency and phase of the returning signal.
Liquid Crystal Display - Cell containing long molecules aligned at each surface and 90 degrees apart. Polarised light is rotated through the cell with no applied voltage. Cell becomes opaque when a voltage is applied as the molecules align to the electric field. However, the shutter needs to open in a few ns and the LCD is too slow with transition times of > 10 μs.

## Slide 13
Suitably Fast Shutters
Electro-optic - Pockels cell shutter using fast switching of polarisation to block and transmit light.
Acousto-optic - A piezoelectric device transmits a sound wave through a quartz crystal to produce a diffraction grating. This grating then deflect light.

## Slide 14
Suitably Fast Shutters
Electro-optic - Pockels cell shutter using fast switching of polarisation to block and transmit light. However, more than 50% of returning signal is lost.
Acousto-optic - A piezoelectric device transmits a sound wave through a quartz crystal to produce a diffraction grating. This grating then deflect light.

## Slide 15
Suitably Fast Shutters
Electro-optic - Pockels cell shutter using fast switching of polarisation to block and transmit light. However, more than 50% of returning signal is lost.
Acousto-optic - A piezoelectric device transmits a sound wave through a quartz crystal to produce a diffraction grating. This grating then deflect light. However, the speed of the shutter is limited to the speed of sound in the crystal and it is only fast enough if the return signal beamwidth is very small ~ 1 micron.

## Slide 16
Pockels Cell Shutter
Pockels cell picture taken from website www.leysop.com
Example
Wavelength range:
0.3 – 1.2μm
Optical Rise time:
< 1.0ns
Contrast:
> 1000:1

## Slide 17
Pockels Cell Shutter
Example
Pockels cell picture taken from website www.leysop.com
Physical length:
42mm
Physical diameter:
35mm
Insertion loss:
< 4%

## Slide 18
Pockels Cell Shutter
Schematic
Light is polarised before entering the Pockels cell crystal. With no applied voltage the light is blocked.
Blocked
Pockel cell Crystal
Polariod
Polariod

## Slide 19
Pockels Cell Shutter
Schematic
With an applied high voltage the polarisation of the light is rotated. The light can then pass through the second polariod a reach the detector.
Pockel cell Crystal
Applied kV Voltage
Polariod
Polariod
To
Detector

## Slide 20
Malus's Law
The major disadvantage of introducing a Pockels cell shutter before the C-SPAD is the loss of signal intensity due to Malus's Law.
For a perfect polariser aligned by θ to polarised light of intensity I0, the output intensity equals:
I = I0cos2θ
Only the intensity component that is parallel to the polariser's transmisson axis is transmitted.

## Slide 21
Malus's Law
Unpolarised light consists of a random mixture of polarisations. The average over this random mixture is the average of cos2θ from 0 to 90o, which equals ½.
Therefore the intensity of unpolarised light through a perfect polariser is reduced by half.
Polarisers are not perfect and so transmission is less than 50%, although this is small using calcite glass polarisers.

## Slide 22
Further issues
The Pockels cell must be electronically switched at high voltage. This reduces gating time to 10-15ns.
The Pockels cell will not block all wavelengths of light so it is positioned after the dichroic mirror in the return path and experiences mostly green light.
Altimetry or LEO satellites could have a sloping track in a narrow a range gate and searching is difficult. Therefore this technique works best for Lageos or HEO satellites.

## Slide 23
Conclusion? Install a Pockels cell?
A very fast shutter would benefit Lageos and HEO SLR by reducing daytime noise.
The best shutter option is a Pockels cell and all of the obstacles encountered in planning for the installation have been overcome.
The disadvantage of this shutter is a 50% loss of return signal.
The advantage is the close gating that reduces the number of lost shots due to daytime noise.

## Slide 24
Alternative Detector?
An alternative option that would give the same advantage of close gating would be to switch to an MCP-PMT detector.
An MCP-PMT detect can be gated even quicker than a Pockels cell shutter.
Also this detector has much less dark noise compared to the SPAD.

## Slide 25
MCP-PMT Detector?

## Slide 26
MCP-PMT Detector?
Choice of MCP-PMT from Photek or Hamamatsu:
Photek PMT210 S2
Very fast gating
Quantum efficiency = 12%
Jitter = 30ps
Hamamatsu MCP-PMT R5916U-64
Very fast gating
Quantum efficiency = 40%
Jitter = 110ps
Installed at Borowiec
Testing at Herstmonceux

## Slide 27
MCP-PMT Detector?
Photek
Testing at Herstmonceux