## Slide 1: Space-Based Calibration of HF Radars using the Precision Expandable Radar Calibration Sphere (PERCS)
Paul A. Bernhardt
Plasma Physics Division, Naval Research Laboratory
Washington, DC 20375
bern@ppd.nrl.navy.mil
Phone: 202-767-0196
AMOS Conference
Maui, Hawaii
14 September 2007
Work Sponsored by ONR

## Slide 2: Radar Calibration Sphere
Calibration Applications
  Systems: SuperDARN Radars and High Frequency Active Auroral Research Program (HAARP) Array Calibration
  Measurements: Absolute Radar Sensitivity and Absolute Range Determination
  Science Applications
    Tracking and Strength of High Latitude Field Aligned Irregularities
    Interactions of High Power Radio Waves in the Ionosphere
    Determination of Electron Densities in Meteor Head Echoes
Specifications
  Frequency Range: 2.8 to 28 MHz
  Size
    ~1 m Stowed Configuration less at Launch
    ~10 m Diameter After Deployment
  Cross Section Accuracy Within 0.5 dB from Any Direction
  Polar Orbit Inclination (> 80)
  Low Earth Orbit (LEO, 600 to 1000 km Altitude)
  Long Life (> 3 years)
Implementation: Precision Expandable Radar Calibration Sphere (PERCS)
  Wire Frame Hoberman Sphere
  60, 240, or more Vertices

## Slide 3: PERCS Calibration of the NSF SuperDARN Radar Systems
Halley
Sanae
East & South
Syowa
Kerguelen
TIGER
SuperDARN
An International Radar Network for Studying the Earth's Upper Atmosphere, Ionosphere, and Connection into Space
-40 Latitude
PERCS Orbit
King Salmon
Kodiak
Prince George
Saskatoon
Kapuskasing
Goose Bay
Stokkseyri
þykkvybær
Hankasalmi
+40 Latitude
PERCS Orbit
PERCS Operational Utility: (1) Absolute System Calibration from 8 to 20 MHz
(2) Characterize Effects of Ionospheric Refraction

## Slide 4: Currently “Arbitrary Units” Used for All SuperDARN Observations of Backscatter Power from Field Aligned Irregularities in the Ionosphere
PERCS Calibration of SuperDARN Radar
  Absolute Return Power Determination
  Relate Measurements from one Experiment to the Next
Hughes et al., 2003
Bristow 2004

## Slide 5
HAARP Instrument Experiments with the PERCS
HAARP Facility
PERCS Orbit
HAARP HF Beam
HAARP Antenna Array Under Construction
PERCS Operational Utility
  Absolute Calibration of HAARP Antenna Pattern from 2.8 to 10 MHz
  Precise Measurements of Performance for HF Radars that Support HAARP

## Slide 6: PERCS Applications for HAARP
HF Antenna Calibration
  Absolute System Sensitivity
  Faraday Rotation Scatter Target
PERCS Orbit
HAARP Array

## Slide 7: Radar Oblique Scatter from PERCS to Detect Two-Stream Instability Waves
E-Layer
PERCS
Electrojet Driven Waves
Ground Radar

## Slide 8: Radar Backscatter from Metalized Spherical Shell
Incident Plane Wave
Scattered Wave
a


## Slide 9: 10 m Spheroid Radar Target

## Slide 10: 10-meter Wire Frame Radar Reflectors

## Slide 11: Computed Radar Cross Sections for Two Observation Directions

## Slide 12: Computed Radar Cross Section for V60 Wire Frame

## Slide 13: Maximum Variation in Radar Cross Section with View Angle

## Slide 14: V60 Radar Cross Section Variation with Look Direction and Radar Frequency
20 MHz
23 MHz
26 MHz
30 MHz
33 MHz
37 MHz
(a)
(b)
(c)
(d)
(e)
(f)
500
0
500
0
500
0
500
0
500
0
500
0
Radar Cross Section (m2)

## Slide 15: V60 Wire Frame Tuned for Minimum RCS Variation
Tuned V60 Wire Frame Properties
  Radius to Vertex 5 m
  30 Edges with Length 1,53 m
  60 Edges with Length 2.29 m
  Area of Pentagons 9.03 m2
  Area of Hexagons 9.34 m2

## Slide 16: Hoberman Sphere as Radar Calibration Target
Hoberman Associates, Inc. 40 Worth Street, Suite 1680 New York, NY 10013 Tel: (212) 349 7919 Fax: (212) 349 7935 e-mail: associates@hoberman.com
Concept and Tasks
  Design Structure Based on Transformable Sphere
  Calculate Radar Cross Section of Hoberman Sphere Wire Frame
  Construct Sphere with Remote or Self Deployment
  Launch in Rocket or Space Shuttle
US Patent Number 4,942,700, Hoberman 1990
Reversibly Expandable Double-Curved Truss Structure

## Slide 17: V60 Radar Reflector with Two Scissors per Edge

## Slide 18: Drag Limitations on Lifetime of 10 meter Spherical Radar Target

## Slide 19: Precision Expandable Radar Calibration Sphere (PERCS)
Develop Aspect Insensitive Target for Calibration of Ground HF Radars and HF High Power Transmitters
  Space Weather Radar Systems (SuperDARN)
  High Frequency Active Auroral Research Program (HAARP)
OPERATIONAL CAPABILITY ADDRESSED
PROGRAM APPROACH and OBJECTIVES
TECHNICAL APPROACH and OBJECTIVES
Space Demonstration in FY10 (36-Month)
  Science/Modeling, MicroSat (1), and Radar and Laser Ground Data Assessment
  Launch into High Inclination 600 km Orbit
  ~Five Years of On-Orbit Ops (Depends on Atmospheric Drag)
Deliverables: Science & Modeling; One 60 or 240 Vertex Hoberman Sphere; System Integration/Test; Ground Data/Processing Systems
Launch Vehicle by USAF/STP (Secondary Payload)
Place Calibration Target for HF Radar Systems in Low Earth Orbit with Known Radar Cross Section (RCS)
Demonstrate Deployment of Large Polyhedral Structure in Space
Self Expanding Wire Frame using Hoberman Sphere Technology
Low Atmospheric Drag Using Open Frame Configuration with No Impact on RCS Properties
Baseline Design: 10 Meter Diameter Target with Operational Radio Frequencies Up to 40 MHz
HF Radar Calibration Target in Space
Deployment of a V60 Hoberman Sphere
Notes: <number>