## Slide 1: Precision Expandable Radar Calibration Sphere (PERCS) Experiment Concept
Develop Aspect Insensitive Target for Calibration of Ground HF Radars and HF High Power Transmitters
  Space Weather Radars (SuperDARN)
  Ionospheric Heaters (HAARP, EISCAT)
Calibrated Optical Target for Ground Satellite Laser Ranging Systems
GROUND SYSTEMS SUPPORTED
Comparisons to Alternatives
TECHNICAL APPROACH and OBJECTIVES
Metal Balloon in Low Earth Orbit
  High Atmospheric Drag Limits Lifetime
  High Fabrication and Materials Cost
Aircraft HF Radar Calibration Limited in Area
Existing Objects in Low Earth Orbit (LEO) are NOT Usable for HF Radar Calibration
  Existing Radar Calibration Spheres are Too Small (ANDE – 1 meter diameter)
  Large Satellites have Irregular Cross Section (e.g. Space Shuttle, Space Station)
Wire Frame Calibration Target for HF Radar Systems in Low Earth Orbit with Known Radar Cross Section (RCS)
Deployment of Large Polyhedral Structure in Space with ~ 5 Year On-Orbit Operations
Low Atmospheric Drag Using Open Frame Configuration with No Impact on RCS Properties
Corner Cube Reflectors at the Vertices of Spherical Polyhedron Provides Optical Calibration Source
Baseline Design: 10 Meter Diameter Target with HF Radio Frequencies Up to 40 MHz
HF Radar and LRS Calibration Target in Space
Deployment of a V60
Wire-Frame Sphere
Design Specifications
Deployment from 1.2 to 10 meters Diameter
1080 Retro-Reflectors Around 180 Vertex Sphere
Complementary Experiments: ANDE
Notes: <number>